## Slide 1
Binary coded decimal (BCD)
Binary Coded Decimal (BCD) gives a 4 bits code for each decimal digit.
Decimal Symbol | BCD Digits
0 | 0000
1 | 0001
2 | 0010
3 | 0011
4 | 0100
5 | 0101
6 | 0110
7 | 0111
8 | 1000
9 | 1001
10 | 0001 0000

## Slide 2
Excess 3 Code
The following table shows the various binary codes for decimal digits 0 to 9.
Decimal Digit | 8421 Code | Excess 3 Code
0 | 0000 | 0011
1 | 0001 | 0100
2 | 0010 | 0101
3 | 0011 | 0110
4 | 0100 | 0111
5 | 0101 | 1000
6 | 0110 | 1001
7 | 0111 | 1010
8 | 1000 | 1011
9 | 1001 | 1100

## Slide 3
Invalid cases in 8421 BCD code are:
Invalid cases in Ex-3 BCD code are:
There are 6 invalid cases in these codes

## Slide 4
Gray Code
The following table shows the 4-bit Gray codes corresponding to each 4-bit binary code.
Decimal Number | Binary Code | Gray Code
0 | 0000 | 0000
1 | 0001 | 0001
2 | 0010 | 0011
3 | 0011 | 0010
4 | 0100 | 0110
5 | 0101 | 0111
6 | 0110 | 0101
7 | 0111 | 0100
8 | 1000 | 1100
9 | 1001 | 1101
10 | 1010 | 1111
11 | 1011 | 1110
12 | 1100 | 1010
13 | 1101 | 1011
14 | 1110 | 1001
15 | 1111 | 1000

## Slide 5
This code doesn’t have any weights. So, it is an un-weighted code.
In the above table, the successive Gray codes are differed in one bit position only. Hence, this code is called as unit distance code.

## Slide 6
Follow these steps for converting a binary code into its equivalent Gray code.
Write the left of MSB in binary code.
Compare the successive two bits starting from MSB in binary code. If the 2 bits are same, then the output is zero. Otherwise, output is one.
Repeat the above step till the LSB of Gray code is obtained.
Binary code to Gray Code Conversion

## Slide 7
Example
From the table, we know that the Gray code corresponding to binary code 1000 is 1100. Now, let us verify it by using the above procedure. Given, binary code is 1000.
Step 1: Write the left of MSB in binary code.
Step 2: By comparing successive two bits of binary code, we will get the gray code as 1100.

## Slide 8
Gray code to Binary Code Conversion