Diode Switching Circuits

Basic Concepts:

Diode switching circuits typically contain two or more diodes, each of which is connected to an independent voltage source. Understanding the operation of a diode switching circuit depends on determining which diodes, if any, are forward biased and which, if any, are reverse biased. The key to this determination is remembering that      a diode is forward biased only if its anode is positive with respect to its cathode      (see Fig. 2-1). One of the very import applications of diode switching circuits is      logic gates.

Fig. 2-1

Logic Gates:

Diodes can be used to form logic gates, which perform some of the logic operations required in digital computers.

(  OR Gate:

It has output when there a signal in any input channels (see Fig. 2-2).

| Input voltages | State of diodes | Output voltage |
| --- | --- | --- |
| VA | VB | D1 | D2 | Vo |
| 0 | 0 | off | off | 0 |
| 0 | 1 | off | on | 1 |
| 1 | 0 | on | off | 1 |
| 1 | 1 | on | on | 1 |

Fig. 2-2

(  AND Gate:

It has output only when all inputs are present (see Fig. 2-3).

| Input voltages | State of diodes | Output voltage |
| --- | --- | --- |
| VA | VB | D1 | D2 | Vo |
| 0 | 0 | on | on | 0 |
| 0 | 1 | on | off | 0 |
| 1 | 0 | off | on | 0 |
| 1 | 1 | off | off | 1 |

Fig. 2-3

Example 2-1:

Determine which diodes are forward biased and which are reverse biased in the circuits shown in Fig. 2-4. Assuming a 0.7-V drop across each forward-biased diode, determine the output voltage Vo.

Fig. 2-4

Solution:

Appling a golden rule, a diode is forward biased when

,  yields:

In (a) the net forward-biasing voltage between supply and input for each diode is

D1 & D3: 	+5 - (+5) = 0V,

D2 & D4: 	+5 - (-5) = 10V.

Therefore, D2 and D4 are forward biased and D1 and D3 are reverse biased.

Vo = -5 + 0.7 = -4.3V.

While in (b) the net forward-biasing voltage between supply and input for each diode is

D1: 	+15 - (+5) = +10V,

D2: 	+15 - 0 = +15V,

D3: 	+15 - (-10) = +25V.

Therefore, D3 is forward biased and D1 and D2 are reverse biased.

Vo = -10 + 0.7 = -9.3V.

Finally, in (c) the net forward-biasing voltage between supply and input for each    diode is

D1:   -5 - (-10) = +5V,

D2:   +5 - (-10) = +15V.

Therefore, D2 is forward biased and D1 is reverse biased.

Vo = +5 - 0.7 = +4.3V.

Exercise:

Determine Vo and I  for each circuit in Fig. 2-5. Assume that each of the diodes in these circuits has a forward voltage drop of  0.7 V.

Fig. 2-5