Superposition Theorem

The current through, or voltage across, an element in a linear bilateral network is equal to the algebraic sum of the currents or voltages produced independently by each source.

The total power delivered to a resistive element must be determined using the total current through or the total voltage across the element and cannot be determined by a simple sum of the power levels established by each source.

EXAMPLE: Determine I1 for the network.

Solution:

1) Setting E = 0 V

2) Setting I = zero

EXAMPLE: Using superposition, determine the current through the 4-resistor

Solution:

1) Considering the effects of a 54-V source

2) Considering the effects of the 48-V source

EXAMPLE: Using superposition, find the current through the 6- resistor of the network, and find it's power.

Solution:

1) Considering the effect of the 36-V source

2) Considering the effect of the 9-A source

EXAMPLE: Using the principle of superposition, find the current I2 through the 12-k resistor.

Solution:

1) Considering the effect of the 6-mA

2) Considering the effect of the 9-V voltage source